## Slide 1
MechaRAMS
Team 999
Under the Hood: the Vision & Trajectory Code
A programmer's tour — classes, math, configuration, and calibration
Follow-up to “Robot Localization & Precision Driving” — assumes you know the algorithms from that deck
For students and mentors · Summer 2026

## Slide 2
MechaRAMS
Team 999
What this deck covers
2
The class map: what we wrote, what the vendors give us, and how the pieces talk.
The pipeline end-to-end: camera photons → accepted measurement in the estimator.
The math behind each stage — including the calculus where it matters.
Every important configuration constant, and the calibration routine that replaces each guess with a measurement.
Project: VisionTestingAndCalibration (repo FRC999/2027Prototyping) — WPILib 2026 command robot, ~2,800 lines + 45 unit tests. Deep dive companions: CODE_WALKTHROUGH_VISION_AND_TRAJECTORY.md (line-by-line) and ARCHITECTURE_AND_DEPLOYMENT.md.

## Slide 3
MechaRAMS
Team 999
Where each piece runs
3
Orange Pi 5 (coprocessor)
PhotonVision
• detects tags in each frame
• multi-tag + single-tag PnP solves
• publishes over NetworkTables
Images never leave the Pi — only tag observations do.
roboRIO (robot code — ours)
• VisionIO reads observations
• VisionPolicy gates + weighs
• TrigSolve / covariance models
• CTRE estimator fuses at 250 Hz
• PathPlanner + precision command
• AdvantageKit logs everything
Laptop
• Driver Station
• AdvantageScope (live + replay)
• PathPlanner path editor
• PhotonVision web UI (config + calibration)
DESIGN RULE (AGENTS.md)
Final pose fusion and drivetrain control stay on the roboRIO. The Pi is a measurement source, never the brain. One Pi failing degrades vision; it cannot take down driving.

## Slide 4
MechaRAMS
Team 999
The class map — ours vs. vendor
4
OURS (frc.robot)
VENDOR LIBRARY
WPILIB
Vision
subsystems/vision/
Vision.java (orchestrator)
VisionPolicy.java (pure gates/σ)
SingleTagTrigSolver.java (pure)
VisionIO.java (@AutoLog iface)
VisionIOPhotonVision.java
VisionIOPhotonVisionSim.java
photonlib: PhotonCamera,
simulation.VisionSystemSim
AdvantageKit: Logger,
@AutoLog inputs
Drive & fuse
DriveSubsystem.java
extends CTRE SwerveDrivetrain
sampleHeadingAt(), reset time
CTRE Phoenix 6: SwerveDrivetrain
(Kalman estimator + 250 Hz
odometry thread + pose buffer)
pathplannerlib: AutoBuilder,
FollowPathCommand
wpimath: Kalman internals
Commands & aim
commands/
DriveToPosePrecisionCommand
DriveAndAimCommand
AimAtGoalCommand
DriveManuallyCommand
util/AimingCalculator (pure)
RobotContainer (wiring + chooser)
wpimath: ProfiledPIDController,
TrapezoidProfile, geometry
Pure classes (no hardware imports) are the unit-tested core: VisionPolicy, SingleTagTrigSolver, AimingCalculator — 100% line coverage, enforced by a JaCoCo ≥90% build gate.

## Slide 5
MechaRAMS
Team 999
The fusion pipeline — one frame's journey
5
1. Capture
PhotonVision solves tags; result + capture timestamp on NT
2. VisionIO
updateInputs() fills PoseObservation records; Logger.processInputs makes it replayable
3. Gates
VisionPolicy.rejectionReason(): NO_TAGS / NON_FINITE / BAD_Z / OUTSIDE_FIELD / TOO_FAR / SINGLE_TAG_AMBIGUOUS
4. Strategy
single-tag + TRIG_SOLVE mode → replace XY via odometry-buffer heading (fallback: PnP)
5. Weigh
standardDeviations(): isotropic or anisotropic σ; single-tag σθ = +∞ always
6. Fuse
drive.addVisionMeasurement(pose, fpgaToCurrentTime(t), σ) → CTRE Kalman applies it AT ITS TIMESTAMP

## Slide 6
MechaRAMS
Team 999
The IO layer — why vision is split in three
6
VisionIO is an interface; the real robot binds VisionIOPhotonVision, the simulator binds VisionIOPhotonVisionSim. One swap in RobotContainer.
Every input crosses through @AutoLog → recorded to the .wpilog → any match can be REPLAYED against modified code on a laptop.
This is the direct fix for 2026's “no logging” finding — tuning arguments become replay experiments.
public static record PoseObservation(
double timestampSeconds,
Pose3d robotPose,
double ambiguity,
int tagCount,
double averageTagDistanceMeters,
boolean isMultiTag,
int primaryTagId) {}
PoseObservation is the ONLY thing the fusion side sees — the entire camera story in 7 fields.
primaryTagId (added for TrigSolve) anchors the tag lookup and the anisotropic ray angle.
TargetObservation (tx bearing + timestamp) rides alongside for the future boresight fine-aim loop.
// VisionIOPhotonVision — multi-tag branch
Transform3d fieldToCamera =
multitagResult.estimatedPose.best;
Transform3d fieldToRobot =
fieldToCamera.plus(robotToCamera.inverse());
Pose3d robotPose = new Pose3d(
fieldToRobot.getTranslation(),
fieldToRobot.getRotation());

## Slide 7
MechaRAMS
Team 999
The gates — VisionPolicy.rejectionReason()
7
Gate | Constant (value) | Catches
NO_TAGS | — | empty frames
NON_FINITE | NaN/Inf on pose, distance, ambiguity | corrupt data poisoning σ math or slipping past gates
BAD_Z | MAX_ACCEPTED_Z_METERS = 0.25 | 3D solves that put the robot above/below the floor
OUTSIDE_FIELD | FIELD_BORDER_MARGIN_METERS = 0.50 | physically impossible positions
TOO_FAR | MAX_AVERAGE_TAG_DISTANCE_METERS = 5.0 | long-range junk (candidate to relax for multi-tag)
SINGLE_TAG_AMBIGUOUS | MAX_SINGLE_TAG_AMBIGUITY = 0.20 (also rejects unknown −1) | the mirror problem (kept ON under TrigSolve for a fair A/B)
DESIGN PRINCIPLE (2026 fix #5)
Rejection is PHYSICAL plausibility only — there is deliberately no “distance from odometry” innovation gate, because that is the gate that locked in drift in 2026. Every rejection logs its enum to Vision/CameraX/LastRejectionReason.

## Slide 8
MechaRAMS
Team 999
Timestamps — the bug you cannot see on a bench
8
PhotonVision stamps frames on the FPGA clock; CTRE's estimator runs on ITS OWN time base. Fusing without converting = fusing at the wrong moment in history.
The fix is one call — but it is a correctness requirement, not a nicety.
sampleHeadingAt() reads the SAME CTRE pose-history buffer the estimator fuses against (POSE_HISTORY_SECONDS = 0.6), so TrigSolve's heading and the fusion see one consistent timeline.
Odometry samples at ODOMETRY_UPDATE_FREQUENCY_HZ = 250 on the CANivore thread.
// DriveSubsystem
public void addVisionMeasurement(
Pose2d pose, double t, Matrix<N3,N1> std) {
super.addVisionMeasurement(
pose, Utils.fpgaToCurrentTime(t), std);
}
public Optional<Rotation2d> sampleHeadingAt(
double fpgaTimestampSeconds) {
return samplePoseAt(Utils.fpgaToCurrentTime(
fpgaTimestampSeconds))
.map(Pose2d::getRotation);
}
WHY IT MATTERS
At 2 m/s, a 50–100 ms-old frame describes a robot 10–20 cm behind the present. The buffer transform applies each measurement where the robot WAS, then replays odometry forward.

## Slide 9
MechaRAMS
Team 999
The estimator update — the one equation everything feeds
9
x̂ ← x̂ + K (z − x̂) K = P / (P + R) (per axis, conceptually)
x̂ = current estimate · z = camera measurement · P = estimator's own uncertainty · R = σ² we assign the measurement
Everything we compute lands in R. Small σ → K near 1 → the estimate jumps to the camera. Huge σ → K near 0 → frame barely matters. σθ = +∞ is how “never fuse single-tag heading” is implemented — Kθ becomes exactly 0. No special cases, no if-statements in the filter.
The gates protect the assumption behind the math: Kalman filters average Gaussian noise. An ambiguity flip is NOT noise — it is a wrong hypothesis, and averaging with a wrong hypothesis pollutes the state. Reject; never down-weight garbage.
CTRE runs the multi-dimensional version of this at 250 Hz with the pose buffer handling out-of-order measurements. We feed it; we do not reimplement it.

## Slide 10
MechaRAMS
Team 999
Trust math I — the isotropic baseline (and why d²)
10
// VisionPolicy.standardDeviations()
double k = obs.averageTagDistanceMeters();
double base = k * k
/ (obs.tagCount() * obs.tagCount());
xy = LINEAR_STD_DEV_BASELINE * base * camFactor;
LINEAR_STD_DEV_BASELINE = 0.06 m, ANGULAR = 0.08 rad (at 1 m, 1 tag).
÷ tagCount²: more tags → dramatically better solve.
× CAMERA_STD_DEV_FACTORS[i] (all 1.0 until measured — a worse camera should count less).
A LITTLE CALCULUS — why distance-squared
The tag's apparent size s ∝ 1/d. Range is inferred from s, so
d(s) = c/s ⇒ ∂d/∂s = −c/s² = −d²/c
A fixed pixel error Δs therefore produces a range error that grows like d². The covariance model is that derivative, written as a constant.
LIMITATION (deck 1's “circle”)
One σ for both X and Y — direction-blind. The along-ray (range) component is 2–4× noisier than across-ray in reality.

## Slide 11
MechaRAMS
Team 999
Trust math II — the anisotropic model
11
THE MODEL
σ∥ = C∥ · d^E∥ (along camera→tag ray)
σ⊥ = C⊥ · d^E⊥ (across the ray)
Σfield = R(α) · diag(σ∥², σ⊥²) · R(α)ᵀ
α = ray angle in field frame (from primaryTagId's known pose)
Constant | Single-tag | Multi-tag
PARALLEL_COEFF | 0.060 | 0.015
PARALLEL_EXP | 2.0 | 2.0
PERP_COEFF | 0.030 | 0.0075
PERP_EXP | 2.0 | 2.0
Idea from 5940's 2026 code (they fit these curves from logs). 2:1 parallel:perp ratio, matched to the isotropic model at 2 m.
θ keeps the baseline model on purpose — no unfitted second power law.
PROVISIONAL until test step R2 fits real coefficients — and R2 must fit them UNDER the winning single-tag strategy, because TrigSolve changes the error's shape.
Expected effect: stops the “breathing” toward/away from the board — the prime suspect for July's 8 cm post-stop drift.
Toggle: Vision.setCovarianceModel(CovarianceModel.ANISOTROPIC) — every chooser auto pins its model explicitly.

## Slide 12
MechaRAMS
Team 999
TrigSolve — the actual math
12
p_robot = p_tag − R(θ_gyro) · ( t_robot→cam + R_cam · t_cam→tag )
tag's known field position, minus the robot→tag vector rotated by the KNOWN heading. The PnP rotation appears nowhere.
// SingleTagTrigSolver.solve() — the whole trick
Pose3d robotAtOrigin = new Pose3d(0,0,0,
new Rotation3d(0,0,heading.getRadians()));
// field-frame robot->tag vector: cameraToTag's
// rotation is LAST in the chain, so it cannot
// influence this translation
Translation3d robotToTagField = robotAtOrigin
.transformBy(robotToCamera)
.transformBy(cameraToTag)
.getTranslation();
Translation3d pos =
tagPose.getTranslation().minus(robotToTagField);
return new Pose2d(pos.getX(), pos.getY(), heading);
reconstructCameraToTag() inverts the IO composition exactly — no new logged field needed: cameraToTag = Transform3d(observedRobotPose ∘ robotToCamera, tagPose).
The returned rotation is the heading we were GIVEN — never fused back (σθ = +∞). Fusing it would be 2026's circular-feedback bug reborn.
Pinned by unit test: corruptedPnpRotationDoesNotMoveTheSolution — we corrupt the PnP rotation on purpose and assert the answer doesn't move.

## Slide 13
MechaRAMS
Team 999
TrigSolve — wiring and failure handling
13
Runs in Vision (not the IO layer) so it can consult the odometry buffer: heading = drive.sampleHeadingAt(frame timestamp).
Applied AFTER the gates, replacing only the XY of single-tag frames — the same frames are fused in both modes, so the A/B compares strategies, not datasets.
Falls back to PnP per frame when the buffer or tag lookup cannot answer (buffer empty right after boot/reset, unknown tag id).
Known weakness stays visible: a long single-tag-only stretch lets heading drift leak into XY (≈ 3.5 cm/° at 2 m). The conditional future fix — a heading-health PnP fallback — is implemented ONLY if R1/R3 logs show it.
// Vision.periodic() (abridged)
if (strategy == TRIG_SOLVE
&& obs.tagCount() == 1) {
Optional<Pose2d> solved =
trigSolve(cam, obs);
if (solved.isPresent()) {
fusedPose = solved.get();
usedTrigSolve = true; // logged
} // else: PnP
}
LOG CHANNELS
Vision/Summary/TrigSolvedPoses (all trig-solved this loop), Vision/CameraX/LastUsedTrigSolve, Vision/Modes/SingleTagStrategy + CovarianceModel — every log names the configuration that produced it.

## Slide 14
MechaRAMS
Team 999
Pose resets — the quarantine story
14
July 1 sim log: press A to reset → pose snapped correctly → then BOUNCED BACK. Cause: in-flight camera frames captured BEFORE the reset arrived after it and were fused.
Fix layer 1 — isPreResetFrame(): discard any frame whose capture timestamp precedes the last reset.
Fix layer 2 — isResetSuppressed(): a fixed RESET_QUARANTINE_SECONDS = 0.35 window after every reset, because sim-delayed frames can carry timestamps that slip PAST the reset instant.
Related gate: AUTO_VISION_IGNORE_SECONDS = 0.3 at auto start protects the known start pose from a bad first frame. And A/B pose-reset buttons are disabled during enabled autonomous.
// VisionPolicy (pure, unit-tested)
static boolean isPreResetFrame(
double obsT, double lastResetT) {
return obsT < lastResetT;
}
static boolean isResetSuppressed(
double nowT, double lastResetT) {
return nowT - lastResetT
< RESET_QUARANTINE_SECONDS;
}
THE 2026 CONTRAST
2026 re-anchored by hard resetPose() calls MID-MATCH (tag loss, Quest↔LL transitions) — each one discarded filter history and trusted one measurement completely. 2027: resets are a bench/test tool; in a match the filter converges via weighting, never snapping. Suppressed frames are logged to Vision/Summary/ResetSuppressedPoses.

## Slide 15
MechaRAMS
Team 999
DriveToPosePrecisionCommand — internals
15
Three ProfiledPIDControllers (x, y, θ) — each runs a trapezoid motion profile toward the goal, then PID against the PROFILE, not raw error.
Translation output clamped as a VECTOR (magnitude), not per-axis — per-axis clamping distorts the direction by up to √2 on diagonals.
Settle gate: success = staying inside tolerance for PRECISION_SETTLE_SECONDS continuously. Safety timeout ends it unsuccessfully after 4 s.
Constant | Value
TRANSLATION_TOLERANCE | 0.04 m (was 0.03 — runs hit 0.027 m but couldn't HOLD it)
ROTATION_TOLERANCE | 1.5°
SETTLE_SECONDS | 0.25
SAFETY_TIMEOUT | 4.0 s
DRIVE_KP / THETA_KP | 3.2 / 4.5 (KD 0)
MAX v / a | 1.6 m/s, 2.5 m/s²
A LITTLE CALCULUS — the trapezoid profile
The profile is v(t): accelerate at aₘₐₓ, cruise at vₘₐₓ, decelerate so v → 0 exactly at the goal. Position is its integral:
x(t) = ∫ v(t) dt
The deceleration point comes from v² = 2a·d — start braking when remaining distance d = v²/2a. PID then only corrects deviation FROM this profile, so gains stay small and the arrival is not a collision.
HANDOFF WIRING
spatialHandoffAuto(): PathPlanner path .until(pose.x > 3.3).andThen(precision command). The chooser also carries sequential + baseline variants and the AB: configuration matrix.

## Slide 16
MechaRAMS
Team 999
Chassis aiming & shoot-on-move — a fixed-point iteration
16
AimingCalculator: heading to a virtual GOAL_POSITION (7.5, 2.0) — one constant moves when the real target exists. No turret; the chassis is the turret.
Shoot-on-move: while moving, aim at where the goal WILL BE relative to you after the projectile's time of flight. But TOF depends on distance, which depends on the lead... circular.
Solution: iterate. TOF model = 0.25 + 0.08·d seconds; SHOOT_ON_MOVE_ITERATIONS = 15.
DriveAndAimCommand: drive with left stick, ω comes from the aim controller (kP 5.0, tol 1.5°, settle 0.2 s).
WHY 15 ITERATIONS IS ENOUGH
dₙ₊₁ = ||goal − v·TOF(dₙ)|| is a contraction: each pass multiplies the remaining error by roughly |v|·∂TOF/∂d = |v|·0.08 ≈ 0.13 at 1.6 m/s.
0.13¹⁵ ≈ 10⁻¹¹ — converged to machine noise long before iteration 15. (A Banach fixed point, if you want the fancy words.)
The math after the loop recomputes TOF from the FINAL distance — an early Codex review caught that the naive version used the stale one.
UNIT-TESTED
AimingCalculatorTest (5 tests): stationary aim, moving lead direction, TOF consistency, offset handling.

## Slide 17
MechaRAMS
Team 999
The A/B machinery
17
// VisionPolicy — the two contests
public enum SingleTagStrategy
{ PNP, TRIG_SOLVE }
public enum CovarianceModel
{ ISOTROPIC, ANISOTROPIC }
// runtime setters on Vision, logged
// every loop under Vision/Modes/*
Every chooser option routes through withVisionModes(...) — baselines PIN PNP+ISOTROPIC explicitly, so a leftover experiment can never contaminate a baseline run.
Four AB: autos cover the matrix; curved variants add the rotation-sweep stress case.
Decision rule (R5): best WORST-CASE end-pose error over 5 runs.
Chooser option | Strategy / model
Baselines (straight, curved, precision) | PNP + ISOTROPIC (pinned)
AB: ... (TrigSolve) | TRIG_SOLVE + ISOTROPIC
AB: ... (AnisoCov) | PNP + ANISOTROPIC
AB: ... (TrigSolve+AnisoCov) | TRIG_SOLVE + ANISOTROPIC
WHY ENUMS + ONE CODE PATH
Same frames, same gates, same estimator — only the contested layer switches. A/B results are attributable to the algorithm, not to environmental drift between runs. The LoggedDashboardChooser records WHICH auto ran, in the log itself.

## Slide 18
MechaRAMS
Team 999
The logging map — where to look when something is weird
18
Channel | What it tells you
Drive/Pose | the fused pose — the single source of truth every consumer uses
Vision/Summary/AcceptedPoses | all fused vision poses this loop (scatter = your noise level)
Vision/Summary/RejectedPoses + CameraX/LastRejectionReason | what was thrown away and WHY (enum, not a string)
Vision/Summary/ResetSuppressedPoses / AutoSuppressedPoses | quarantine + auto-start suppression at work
Vision/CameraX/LastInnovationMeters | disagreement between camera and estimator — large + persistent = calibration/extrinsic problem, NOT a fusion-weight problem
Vision/Modes/* | active SingleTagStrategy + CovarianceModel — every run self-describes
DriveToPose/* , Aim/* | target vs measured, errors, settle progress, timeout flags
Rule from AGENTS.md: every fused pose, rejection, and mode is logged — “why did the robot think it was there?” must always be answerable from the .wpilog alone.

## Slide 19
MechaRAMS
Team 999
Tests — what guards the math
19
Suite | Tests | Pins down
VisionPolicyTest | 31 | every gate incl. NaN/−1 ambiguity edge cases, both σ models, quarantine, stale-bearing logic
SingleTagTrigSolverTest | 6 | the algebra + corruptedPnpRotationDoesNotMoveTheSolution
AimingCalculatorTest | 5 | aim geometry, shoot-on-move convergence
DriveToPosePrecisionMathTest | 3 | vector clamp, tolerance math
JaCoCo gate wired into ./gradlew check: ≥90% line coverage required on VisionPolicy, SingleTagTrigSolver, AimingCalculator (all currently 100%). Hardware-bound classes are validated by the sim/robot test plan instead.
Workflow discipline: sim first, always — VisionIOPhotonVisionSim produces real PhotonVision frames desktop-side (OV9782 model: 1280×800, 84° FOV, 50 fps, ~30 ms latency, pixel noise), so the whole pipeline runs before any hardware exists.
Canonical build (Windows): JAVA_HOME=C:\Users\Public\wpilib\2026\jdk .\gradlew.bat compileJava test

## Slide 20
MechaRAMS
Team 999
Calibration routines — replacing every guess with a measurement
20
Stage | Routine | Updates
2 Intrinsics | PhotonVision ChArUco calibration per camera at match resolution; mean reprojection error well under 1 px | stored in PhotonVision per camera
3 Extrinsics | measure each lens (x,y,z) + (roll,pitch,yaw) from robot origin; verify vs surveyed pose | ROBOT_TO_*_CAMERA (code + PhotonVision, must match)
4 Accuracy grid | 4–6 surveyed floor poses, static + slow-moving, all camera orientations | STD_DEV baselines, CAMERA_STD_DEV_FACTORS, gate values
5 SysId | quasistatic + dynamic runs (D-pad selects routine) | SwerveConstants gains, WHEEL_RADIUS
R2 fit | stationary scatter vs distance, fit under the WINNING single-tag strategy | ANISO_* coefficients (provisional → measured)
Provisional-value rule (AGENTS.md): unmeasured constants are MARKED provisional in code comments — never silently guessed. If you touch a lens or mount, its calibration is void.

## Slide 21
MechaRAMS
Team 999
Configuration quick reference
21
Group | Key constants (Constants.java)
Cameras | names front-left/front-right (+back-*), ROBOT_TO_* transforms (x .23, y ±.24, z .43, pitch −18°, yaw ±18°), CAMERA_STD_DEV_FACTORS
Gates | Z 0.25 · border 0.50 · ambiguity 0.20 · distance 5.0 · staleness 0.25 s
Trust | LINEAR 0.06 / ANGULAR 0.08 baselines · ANISO_* (provisional) · σθ single-tag = +∞
Timing | 250 Hz odometry · 0.6 s pose history · auto-ignore 0.3 s · reset quarantine 0.35 s
Precision | tol 0.04 m / 1.5° · settle 0.25 s · timeout 4 s · kP 3.2/4.5 · v≤1.6, a≤2.5
Aim | GOAL (7.5, 2.0) · kP 5.0 · tol 1.5° · TOF 0.25+0.08d · 15 iterations
Board | tags 1 & 2 @ (6.0, 1.75/2.25, 1.05 m), 0.1651 m, facing −X · field 8×4 m
All values live in Constants.java with idea-traceability comments — every number cites the team/idea it came from.

## Slide 22
Programmer takeaways
1. Pure math lives in pure classes. VisionPolicy / SingleTagTrigSolver / AimingCalculator have no hardware imports — that is why they are 100% covered and why the A/B is trustworthy.
2. The estimator is fed, not fought. We put our effort into R (the trust), the gates, and the timestamps — and let the vendor Kalman do its one job.
3. Every constant is either measured or marked provisional. The calibration stages exist to burn down the provisional list. Know which side each number is on before trusting a run.
Read next: CODE_WALKTHROUGH_VISION_AND_TRAJECTORY.md · ALGORITHM_COMPARISON_AND_EXPECTATIONS.md · AGENTS.md