## Slide 1
MechaRAMS
Team 999
Robot Localization & Precision Driving
The algorithms we are testing for 2027 — and what we learned in 2026
For students and mentors · Summer 2026

## Slide 2
MechaRAMS
Team 999
Agenda
2
1
Where am I?
Localization: odometry, AprilTags, multi-tag, single-tag PnP vs TrigSolve, trust models
2
How do I drive there?
Trajectory: path following, drive-to-pose, and the handoff between them
3
2026 → 2027
What we ran last season, what hurt us, and what changes
4
How we decide
A/B testing, one competition configuration, what the same data tells us for free

## Slide 3
MechaRAMS
Team 999
Our robot constantly answers two questions
3
1. “Where am I?”
Localization — combine wheel counting, a gyro, and camera views of AprilTags into one continuous position estimate.
2. “How do I drive there?”
Trajectory — cover distance quickly, then arrive at an exact spot. Two different jobs, two different tools.

## Slide 4
Part 1
“Where am I?”
Localization — from wheel counts and street signs to one trusted position
4

## Slide 5
MechaRAMS
Team 999
AprilTags — street signs with known addresses
5
Each tag is a black-and-white square whose exact position on the field is published before the season — a street sign with a known address.
A camera reads the sign and works backwards: “if that sign looks like THAT from here, I must be standing HERE.”
Everything in Part 1 is about how well we do that “working backwards” — especially when the view is bad.
EXAMPLE
You see the “Main St / 5th Ave” sign at a 45° angle, half a block away. You instantly know roughly where you stand. The robot does the same — 50 times per second.
Why cameras at all? Because wheels lie (next slide).
a 36h11 AprilTag (what our cameras look for)

## Slide 6
MechaRAMS
Team 999
Algorithm 1 — Wheel odometry + gyro
6
PROBLEM IT SOLVES
Gives a smooth position estimate 250× per second, always available — cameras cannot do that (30–50 fps, and tags are not always visible).
Counts wheel rotations + uses the gyro (an electronic inner ear).
Like crossing a room with your eyes closed, counting steps: smooth, but every wheel slip is a miscounted step.
Errors pile up → it drifts. It is the base layer, never the whole answer.
EXAMPLE
After 10 s of driving, wheels-only can be off by tens of cm. Each camera fix snaps the error back down — “opening your eyes” for a moment.
Always ON — every configuration we test keeps this as the base layer.

## Slide 7
MechaRAMS
Team 999
Algorithm 2 — Multi-tag solve
7
PROBLEM IT SOLVES
Pins down position AND direction almost perfectly whenever one camera sees two (or more) tags in the same picture.
Two landmarks in one view → only one spot on the field fits both.
This is the only measurement whose DIRECTION we trust — it also keeps the gyro honest.
Not part of the A/B contest: every configuration uses it whenever 2 tags are visible.
EXAMPLE
Seeing both the corner drugstore AND the church tower — there is exactly one street corner where both look like that.
The real question: what do we do when only ONE tag is visible?

## Slide 8
MechaRAMS
Team 999
The single-tag problem — where the real contest is
8
One tag in view happens a lot: during turns, at sharp angles, at the edge of the camera image, far away.
Our curved test path was designed to create exactly these moments (a 25° rotation sweep mid-path).
Algorithms 3 and 4 are two competing answers to the same question: what is a single tag worth?
Algorithm 3 — Single-tag PnP
The baseline. Guess the tag's tilt from the picture, work backwards to the robot. Vulnerable to the “mirror problem.”
Algorithm 4 — TrigSolve
The challenger. Skip the tilt guess entirely — use the direction we already know from the gyro. New for 2027, under test.

## Slide 9
MechaRAMS
Team 999
Algorithm 3 — Single-tag PnP (baseline)
9
PROBLEM IT SOLVES
Gets a full position from just ONE tag — no help from any other sensor. Works even if the gyro is wrong.
Looks at how the tag's square shape is distorted in the picture → guesses the tag's position AND tilt → works backwards.
Weakness: judging the tilt of a flat square from far away is genuinely hard.
A poster angled 20° left vs 20° right looks almost identical across a room — the computer has the same problem (“ambiguity”).
EXAMPLE
Robot approaches at an angle, sees one tag at 3 m. PnP sometimes picks the mirror-image tilt — and reports a position decimeters off.
Today we protect ourselves with an “ambiguity gate” — throw away suspicious frames. A bandage, not a cure.

## Slide 10
MechaRAMS
Team 999
Why a wrong tilt is so costly — the lever arm
10
We never trust the direction PnP reports (2026 lesson). But the tilt guess still participates in computing the POSITION.
A wrong tilt swings the computed position around the tag like a lever arm.
The farther the tag, the longer the lever — small tilt error, big position error.
A LITTLE MATH
position error ≈ tilt error (radians) × distance
A few degrees of tilt noise at 2 m → several cm of error.
A full mirror flip → decimeters, in one frame.
The error is bimodal: usually fine, occasionally terrible. Competition cares about the occasional terrible frame.

## Slide 11
MechaRAMS
Team 999
Algorithm 4 — Single-tag TrigSolve (challenger)
11
PROBLEM IT SOLVES
Removes the unreliable tilt guess from single-tag frames. The mirror problem physically cannot affect it — error becomes small and smooth instead of occasionally huge.
Key insight: the robot already knows which way it is facing (gyro, kept honest by multi-tag frames).
Uses only the EASY camera measurements: direction to the tag (very precise) and distance (decent).
Known facing + direction & range + tag's known address → position.
EXAMPLE
“The sign is 2 m ahead-and-a-bit-left, and I know I’m facing the board → I must be standing HERE.”
Idea from FRC 6328; now built into PhotonVision; team 1678 raced it all season. We test it against PnP.

## Slide 12
MechaRAMS
Team 999
PnP vs TrigSolve — they fail in OPPOSITE ways
12
 | Single-tag PnP | TrigSolve
Mirror problem (ambiguity) | VULNERABLE — decimeter jumps | IMMUNE — tilt drops out
Gyro / heading drift | IMMUNE — uses no gyro | VULNERABLE — inherits gyro error
Error character | Bimodal: fine or terrible | Smooth: grows gently with heading error
Best case | Close range, head-on views, or a broken gyro | Far / angled views, turns — the common case
A LITTLE MATH: TrigSolve error ≈ heading error × distance ≈ 3.5 cm per degree at 2 m. Our gyro stays within ~0.5° when multi-tag frames keep correcting it → ≤ ~2 cm. That is why opposite failure modes matter: we A/B them with data instead of arguing.

## Slide 13
MechaRAMS
Team 999
How it all merges — the estimator
13
All measurements flow into one running weighted average (a Kalman filter) — like averaging opinions, but listening more to the friend who is usually right.
Every camera measurement carries a trust weight. Bad frames are rejected before they ever enter (impossible positions, too far, too ambiguous).
Odometry + gyro
250× / second
Camera fixes
30–50 / second, gated
ESTIMATOR
weighted average
One trusted pose
for aiming & driving
Every frame is matched to where the robot was when the photo was taken (timestamping) — at 2 m/s a 50–100 ms-old picture is 10–20 cm of travel. Non-negotiable plumbing in every configuration.

## Slide 14
MechaRAMS
Team 999
Algorithms 5 & 6 — how much to trust a camera fix
14
PROBLEM IT SOLVES
States the confidence of each camera measurement so the estimator listens the right amount — in the right DIRECTIONS.
Headlights at night: you know the car’s DIRECTION precisely, but its DISTANCE only roughly. Cameras are the same about tags.
So real uncertainty is an OVAL pointing at the tag — fuzzy along the line to it, sharp across it.
Algorithm 5 (circle, baseline): same trust in every direction. Simple, validated — but over-trusts the fuzzy distance.
Algorithm 6 (oval, challenger): tells the truth about the shape.
EXAMPLE
With the circle, the robot’s belief “breathes” toward/away from the board with each frame — our prime suspect for the 8 cm of drift AFTER the robot stopped (July 1 test).
Honest caveat: the oval’s real size must be MEASURED on the robot first (test step 15). Until then it runs with placeholder numbers.

## Slide 15
Part 2
“How do I drive there?”
Trajectory — fast transit, precise arrival, and when to switch
15

## Slide 16
MechaRAMS
Team 999
Algorithm 7 — Path following (PathPlanner)
16
PROBLEM IT SOLVES
Covers distance FAST and smoothly along a pre-planned route, respecting what the drivetrain can physically do.
Like a dancer performing a memorized routine to music: at each beat, be at this spot.
The catch: it ends when the MUSIC ends — not when you are on your mark.
Our tests: stops ~7 cm from the true target. Fine mid-field; not fine for scoring.
EXAMPLE
The 2026 robot: PathPlanner computed “this path takes 2.0 s” and stopped at t = 2.0 s — wherever the robot actually was. Sometimes fine, sometimes not.

## Slide 17
MechaRAMS
Team 999
Algorithm 8 — Drive-to-pose (precision parking)
17
PROBLEM IT SOLVES
GUARANTEES arrival: finishes only when the robot is actually AT the target — on position, never on the clock.
No route, no clock: drive → measure → correct → repeat.
“Settle” check: must STAY inside the tolerance for a moment — one lucky bounce through the target doesn’t count.
Safety timeout so it can never get stuck forever.
Our tests: ~3 cm. Slower — wrong tool for crossing the field.
EXAMPLE
Parallel parking: you don’t follow a script for 4.0 seconds and stop — you keep correcting until the car is IN the spot.

## Slide 18
MechaRAMS
Team 999
Algorithms 9 & 10 — combining them: the handoff
18
PROBLEM IT SOLVES
Gets BOTH speed and precision: the dancer covers the field, the parker finishes the job. The two options differ only in WHEN to switch.
Alg 9 — Sequential: finish the whole routine, then park. Predictable, kept for debugging — but you wait for the music to end even when you’re already close.
Alg 10 — Spatial (our choice): the moment the robot crosses a line on the floor (x > 3.3 m), abandon the routine and start parking. Faster cycle, parker controls more of the approach.

## Slide 19
MechaRAMS
Team 999
Measured in simulation — July 2026
19
Chart: Final distance from target (cm) — lower is better
| Path following only | Precision only (whole way) | Sequential handoff | Spatial handoff
End-position error | 6.6 | 4.5 | 2.7 | 3.4
Handoffs park 2–3× closer than path-following alone.
Spatial chosen: nearly sequential’s accuracy, faster cycle, no timeouts.
All numbers from replayable simulation logs — the robot-carpet re-run is test steps 16–19.
Decision made 2026-07-01: spatial handoff is the competition pattern; the others remain as debug / baseline tools.

## Slide 20
Part 3
2026 → 2027
What we ran last season, what hurt us, and what changes
20

## Slide 21
MechaRAMS
Team 999
What we ran in 2026
21
2 Limelight cameras (of the 4 we own) + QuestNav headset tracking.
CTRE’s built-in estimator; a state machine chose ONE “best” camera result per loop.
MegaTag2: the Limelight computed poses using the heading we sent it.
Hard gates: reject vision > 0.6–0.8 m from odometry; hard pose resets to re-anchor.
Turret auto-aim computed the hub angle from this fused pose.
It was a thoughtful design.
The MT1/MT2 selection, IMU management, and Quest fallback logic were more sophisticated than most teams’.
The losses were in HOW measurements were weighted and discarded — and in having no way to measure any of it.
Symptom we all remember: global position good enough to drive — but 2–3° of heading error was fatal for shooting, with no way to check it.

## Slide 22
MechaRAMS
Team 999
What actually hurt us — five findings
22
1
Circular heading feedback — MegaTag2 poses are computed FROM the heading we send — then we fused its heading back in. The estimator “confirmed” its own guess; drift locked in.
2
One camera per loop — We picked one “best” camera and threw the other’s valid measurement away. More correct measurements always help — the filter does the weighting.
3
No logging / replay — No structured logs → every tuning argument was guesswork. This was the single biggest gap.
4
Mid-match pose resets — Re-anchoring snapped the pose while driving — visible as aim jumps, and one measurement was trusted completely.
5
Gates that lock in drift — “Reject vision > 0.6 m from odometry” — but when odometry itself drifted past the gate, every CORRECT camera fix got rejected.

## Slide 23
MechaRAMS
Team 999
The 2–3° problem, in numbers
23
A LITTLE MATH
miss distance ≈ heading error (radians) × shot distance
3° × 5 m ≈ 26 cm off at the hub — the difference between scoring and bouncing out.
In 2026, the shot was aimed entirely from the fused global pose — heading error went straight into the shot, invisibly.
Findings 1–5 each nudged the heading or position a little; the shot paid for all of them at once.
The 2027 fixes attack every link: no circular heading (fix 1), more measurements (fix 2), logs to SEE the error (fix 3), no snaps (fix 4), physics-based rejection instead of hard gates (fix 5).

## Slide 24
MechaRAMS
Team 999
2026 → 2027 — what changes
24
 | 2026 season | 2027 prototype
Cameras fused | One “best” per loop | Every valid measurement, every camera
Direction from single tag | Fused (circular feedback) | Never — direction only from multi-tag
Single-tag position | PnP only, gated | PnP vs TrigSolve — decided by A/B test
Trust model | Linear in distance, uncalibrated | distance² law; circle vs oval A/B, then fitted from logs
Bad-frame handling | Hard gates + mid-match resets | Physics-based rejection; resets only when stopped + quarantine
Driving finish | Path ends on the clock | Spatial handoff → drive-to-pose, ends on position
Measurement | None (dashboard only) | AdvantageKit logs — every frame replayable, every decision explainable

## Slide 25
MechaRAMS
Team 999
How we decide — test, don’t argue
25
1
Simulation
Steps 1–12: straight + curved runs, reset test. Same start pose and target for every configuration — numbers compare 1:1.
2
Real robot
Steps 13–19: camera calibration, a static accuracy grid, fitting the oval’s real size, then the same driving tests on carpet.
3
The verdict
Adopt the configuration with the best WORST-CASE error over 5 runs — competition cares about your worst cycle, not your average.
Both contests (PnP vs TrigSolve, circle vs oval) run as A/B switches in the same code — same frames, fair fight, one variable at a time.
45/45 automated tests already guard the math before any run happens.

## Slide 26
MechaRAMS
Team 999
One robot, one configuration — but smart every frame
26
The competition robot runs ONE fixed setup — no driver-switched vision modes. A mode nobody practiced with loses matches.
But the robot DOES switch algorithms — automatically, per camera frame, 50× a second:
Sees 2 tags
→ multi-tag solve (always wins)
Sees 1 tag
→ the A/B winner (PnP or TrigSolve)
No heading available for that frame
→ quiet fallback to PnP
Frame looks impossible
→ rejected, with the reason logged
The game situation picks the algorithm — faster and more reliably than any human could.

## Slide 27
MechaRAMS
Team 999
Bonus — the same logs answer camera placement
27
Camera placement is really the question “what does each camera see, how often, and how well?” — and every test run records exactly that. No extra work.
Cross-eye angle (±18° today — a guess)
The curved runs map when we drop to 1 or 0 visible tags mid-turn. The blind-moment map says whether to widen or narrow the cameras.
2 cameras or 4?
If blind moments happen mostly when the robot rotates away from the board — that is the data-driven trigger for the rear pair (code is already wired for them).
Is a mount bad?
A camera consistently fuzzier than its twin at the same distance has a flexing mount or bad calibration — the error-vs-distance curves expose it immediately.

## Slide 28
MechaRAMS
Team 999
Cheat sheet — which algorithm wins when
28
Situation | What wins
Both tags visible | Multi-tag solve — every configuration agrees
Single tag, angled or far view (common during approaches) | TrigSolve expected — the mirror problem can’t touch it
Curved / rotating trajectory | TrigSolve matters more — turning multiplies single-tag moments
High speed | Timestamping + spatial handoff; fewer clean frames again favors TrigSolve
Parked near the board (final alignment) | Anisotropic “oval” trust — once fitted from robot logs
After a collision / gyro glitch | Plain PnP is safer until a multi-tag view fixes the heading
This is why losing algorithms stay in the code as fallbacks instead of being deleted.

## Slide 29
MechaRAMS
Team 999
Vocabulary
29
PnP (Perspective-n-Point) — the math answering “given how these known points look in my photo, where was the camera?”
Ambiguity — two mirror-image tilts of a flat tag that look nearly identical to the camera.
Odometry — tracking position by counting your own movements (wheels + gyro).
Covariance / std deviation — the “how sure am I?” number on a measurement; the merge listens more to smaller numbers.
Fusion / estimator — the running weighted average combining odometry with camera fixes.
Handoff — switching from the route-follower to the precision parker mid-drive.
Settle — requiring the robot to STAY on target briefly before declaring success.

## Slide 30
Three things to remember
1. Layers, not one magic algorithm. Odometry always runs; cameras correct it; the contests are only about the weakest links (single tags, trust shape).
2. Arrive on position, not on the clock. Paths for transit, drive-to-pose for the finish — the spatial handoff gives us both.
3. Measure, don’t argue. 2026’s biggest gap wasn’t an algorithm — it was having no logs. Now every claim on these slides is testable, and the tests are already written.
Questions?
30